Network Handling in UNIX

		by E.A. Martin

	The ideas presented in this document 
	have evolved from conversations I have
	had with Dave Clark, Larry Allen, Noel 
	Chiappa, and Tom Texeira.


I. Goals of New Network Software

	More than one process may open to
	net device handler

	Speedier net service

	Reasonable size (not very large)

	Sensible application program interface

	Compatible with following versions
	of Unix:
		Csr v6
		Nu v7
		Berkeley v7

		in that kernel mods fit easily
	into all versions and cause minimal or
	no changes to v7 Unixes other than
	adding the net module.  
		and in that application programs
	can run on these different versions
	preferably with no changes.



II. User Interface

Netopen

fds = netopen(devnet, &netdf)
char	devnet[];

struct netdf {
	int	prot1;		Local protocol id -
				currently only internet 
				is supported 
	int	prot2;		Internet protocol id
				e.g. tcp, user datagram, 
				icmp, ggp
	struct in_name	fhost;	Foreign host internet
				address
	int	fsocket;	Foreign socket number for tcp, udp;
				Type for icmp
	int	lsocket;	Local socket number for tcp, udp;
				Identifier for icmp
	} netdf;

opens a read/write connection to a net device 
handler with NINTRUP mode enabled for the
process which issued the call (see ioctl,
NIOCSETP option).

The netdf structure defines which internet packets 
the process wants to read over this fds.  Netdf
fields may be NULL (i.e. 0); a NULL field means
that the field should be ignored when trying to
match an incoming packet.  A NULL prot2 field
indicates that no packets are to be read over 
this fds.

See Section V. for the current connection
definition and dispatch rules.


Errors 

EINVAL	Protocol1 or protocol2 is unknown and cannot
	be handled

EACCES	Another netdef exists which makes it impossible
	to distinguish between the two. 



Close

close(fds)

Closes the net connection and deletes any
packets in net read buffer for this connection.
See Section IV's discussion of the timeout 
issue for some subtleties regarding net close.



Ioctl

ioctl(fds, request, &argp)

Ioctl performs various network connection control
functions.  Request is an integer code which
specifies what ioctl should do; argp is used to
pass information between the calling process and
the net handler.  Please note that &argp is the
expected third argument.

The request codes and their corresponding argps follow:

NIOCSETL	set net mode
NIOCGETL	get net mode

sets and gets the mode for the net connection.
Argp contains an integer with the following bit
definitions:

	NINTRUP	01	send interrupt SIGAIO to process
			when a packet for this connection
			is read into the net handler
			read buffer.  Only one process
			per connection may enable this
			mode.  Netopen opens with
			NINTRUP mode enabled for the process
			issuing the call.

Error

EACCES	NINTRUP enabled by another process.

 
NIOCGETHT	get local net header and tailer sizes

Argp is a two word array; on return from this
option argp[0] contains the number of bytes to
allocate for the packet's local net header and
argp[1] contains the number of bytes to allocate
for the local net tailer.


NIOCGETMAXPKT	get maximum internet packet size
			which may be received

Returns, in argp, the maximum size (in bytes)
internet packet which may be received.


NIOCGETHOST	get internet id of this host

Argp is a four byte array; on return from this
option argp contains the internet address of
this host.


FIONREAD	get read count

returns, in argp, the number of bytes in the first
packet in the net read buffer for this connection.


NIONWRITE	get write count

Argp is the structure:
	char	in_name[4];
	int	maxfrag;

The maximum fragment size which may be sent between 
this host and the foreign host specified in in_name
is returned in maxfrag.


NIOCHGCLR	clear host gateway table

The kernel maintains a routing table of
internet foreign host names and the best 
first hop gateway to which packets destined
for each host should be sent.  This option
clears the host gateway table.  Argp is NULL.

NIOCHGADD	add a host to the host gateway table

Argp is the structure:
	char	fname[4];
	int	gate;

On input, fname should contain an internet
host name and gate should contain the local
net address of the first hop gateway to 
which packets destined for the host should
be sent.  If the host name is already in the
table, this option replaces its current
entry.  If more than 16 entries are specified,
an attempt is made to drop a host for which
no net connection exists.

NIOCGATE	define default gateway

Argp is an integer containing the local
net address of the gateway to which packets,
whose destination host is not in the host
gate table, should be sent.

NIOCGDEL	delete a gateway

Argp is an integer containing the address of
the gateway to be deleted.  All entries in 
the host gate table for that gateway are deleted; 
the default gateway is set to NULL if it is the 
same as the gateway being deleted.



Write

write(fds, buffad, nbyte)
int	fds;
char	buffad[nbyte];
int	nbyte;

Write packet at buffad[0] to buffad[nbyte]
to the net.  Nbyte must be even. Buffad 
consists of local net header space followed 
by an internet packet. Write to the net is 
done directly from buffad in the process's 
address space.  Write blocks if it cannot be 
processed.

Errors

EINTR  an asynchronous signal came
to the process while write was blocked.
The user may assume that no
net write was done and that it is
appropriate to reissue the write call.

ENOSPC  internet packet being written
is larger than the maximum fragment size
between this connection's local and
foreign hosts.


Read

read(fds, buffad, nbyte)
int	fds;
char	buffad[nbyte];
int	nbyte;

Read reads the first complete internet packet 
for this connection found in the net read buffer 
into buffad. Read returns the number of bytes
read.

The packet read consists of a local net header
followed by an internet packet.

Errors

0  no packet was found in the net read buffer
for this connection

ENOSPC  nbyte is less than the size of the
first packet in the net read buffer for
this connection.  Ioctl, FIONREAD may be used 
to find out the packet's size.



III. Internet Tasks of Kernel and User Process


Internet Header Field	Output 		Output Checked		Input Checked
			Filled by	and/or used by kernel	and/or used by

Header length		user		yes			kernel/user
Version			user		--			  --	
Type of service		user		--			  --
Packet length		user		yes			kernel/user
Id			kernel/user	--			kernel
Fragment offset		user		--			kernel
Flags			user		--			kernel
Time to live		user		--			  --
Protocol		user		--			kernel
Checksum		kernel		--			kernel
Source			kernel		--			kernel/user
Destination		user		yes			kernel
Options			user		--			user

Id field

If the internet id field is 0 in an outgoing packet,
the kernel fills it.  If it is not 0, the kernel does
not fill it. 

Fragmentation and reassembly

The user process does fragmenting; the kernel does
reassembly.

Byte swap/unswap

On output, the user process swaps the integer fields
it fills and the kernel swaps the fields it fills.
On input, the kernel swaps all integer fields,
except option fields, in the internet header.


IV.  Net Handling by the Kernel

Open net connection

When a net connection is opened via
a netopen call from a user process, a
special IFCHR inode is allocated to hold
the net information.  A file descriptor
which points to this inode is returned to
the user process.  

The i_addr[0] - i_addr[7] and i_lastr
fields in the net inode are defined as
follows:
	char		nt_dev;		device address
					(i.e. offset into config table)
	char		nt_flags;	flags
	char		nt_rte;		local net address of first hop dest.
	char		nt_prot;	internet protocol id
	struct in_name	nt_fhost;	foreign host internet name
	int		nt_fskt;	foreign socket number
	int		nt_lskt;	local socket number
	int		nt_proc;	process to signal on pkt read
	struct netino	*nt_forw;	next net inode
	struct netino	*nt_back;	previous net inode

Nt_prot, nt_fhost, nt_fskt, and nt_lskt 
are initialized from the netdf fields
supplied by the calling process.  Nt_proc
is set to the user process id and the 
NINTRUP flag in nt_flag is set. If a foreign
host is specified, nt_rte is set to the first
hop local net address 1) if the foreign host
is on the same net/subnet as this host or
2) if the foreign host is in the hostgate
table.  Otherwise nt_rte is set to NULL.



Close net connection

If no other file descriptors are referencing
the connection's inode, all packets in the net
read buffer which belong to this connection 
are deleted and the inode is deallocated.

If other file descriptors point to this
inode and the process closing the connection
has interrupt on its incoming packets enabled,
this mode (i.e. NINTRUP) is disabled and
nt_proc is set to NULL.


Ioctl for net connection

The NIOCGETL option returns a copy of the
user modifiable bits in the nt_flags field
of the net inode.  The NIOCSETL option sets
bits in this field.  If the NINTRUP flag is
0, the nt_proc field is cleared; if it is 1
and nt_proc is NULL, nt_proc is filled with
the calling process id.

NIOCHGCLR clears the host gate table and the 
nt_rte field in all net inodes.  NIOCHGADD
adds a new entry to the host gate table; or
if the new host is the same as a previous
entry, it replaces the previous entry.  The
net inode list is searched for foreign hosts which 
match the new host; nt_rte is set to the new
gate when a match is found.  If a host must be
dropped to provide room for the new entry,
an attempt is made to drop a host which is not
in the net inode list.  NIOCGATE defines the
default gateway for packets whose foreign host
is not on the same net/subnet or whose foreign 
host is not in the host gateway table.  NIOCGDEL
deletes entries in the host gateway table which 
use the specified gate; it also sets the default 
gate to NULL if it is the gateway being deleted.  
A net inode's nt_rte field is recomputed if it 
equals the gateway being deleted.


Write packet to net

The local net header and various internet header fields 
are filled.  The user process must do packet fragmen-
tation; it must supply space at the beginning of
the packet for the local net header and, if
appropriate, at the end for the local net tailer.

The packet is written to the net directly from
the user process's address space and net write 
status is taken.  Write blocks if the net driver
is busy doing another write.  Care will be taken
to lock out asynchronous signals to the user
process when the actual write is started.  
If this call returns an EINTR error
no net write will have been done and it will
be appropriate for the user process to reissue
the write call.


Read packet from net

Packets are read from the net into a large,
circular kernel buffer.  Various internet
fields are checked; internet reassembly is done.
Using the internet packet's protocol field and
foreign host field and the higher protocol's
foreign and local socket fields, the list of
net inodes is searched to find the best match
with a registered connection.  A pointer to the
"owner" inode is recorded with the packet.  If
NINTRUP is enabled, a SIGNINT signal is sent
to the process specified in nt_proc.

When a user process does a read, the net read buffer
is searched to find a packet for the specified
inode.  If a packet is found, it is copied into
the user process's buffer and dropped from the
kernel net buffer.  If no packet is found for this
inode, the read returns 0.  If the packet in the
net buffer is bigger than the user process's
buffer, ENOSPC error is returned.

A user process reads a complete internet packet
with the local net header and tailer.  This is 
for symmetry with the write call.


Some management details about net read buffer

Structure of packet within net read buffer
	Pointer to next packet
	Pointer to previous packet
	Number of bytes in packet
	Pointer to "owner" inode
	Flags	
		N_FFRAG incomplete packet, first fragment
			into which reassembly is being done
		N_FRAG	incomplete packet, later fragment
			waiting for its first fragment sibling 
			into which it will be copied.
		N_LOCK	packet is being copied into user buffer,
			do not drop it
		N_WANTED
			locked packet's	space is wanted by the
			allocate new buffer space and reenable 
			net receive routine; this routine should 
			be invoked when the packet is unlocked or
			freed.
	Packet

The read buffer is circular so the following info
needs to be maintained about the buffer
	Physical buffer start
	Physical buffer end
	Begin of packet queue
	End of packet queue
	Location where next net read being done
	Flags


Interlocking

When the net read buffer is being searched and/or
modified, other activity on the buffer except
pre-initiated dma into preallocated space in the
buffer must be locked out.  Care must be taken
not to lock activity out for too long.  When a
packet is read from the net, it is important to
allocate buffer space and initiate the next net
read soon so that packets coming from the net
are not missed.

Interlocking Strategies

For User Calls

Netopen
	Allocate and fill inode
	Spl6()  Disable interrupts
	Link inode into net inode chain
	Spl0()  Enable interrupts

Netclose
	If the system file table indicates
	that another fds is open to this
	inode, check whether the closing
	process has NINTRUP enabled on
	the inode.  If it does, set
	NINTRUP in nt_flags to 0 and
	nt_proc to NULL.  The NINTRUP flag
	must be cleared before nt_proc is
	cleared. Return.

	If no other fds is open to the inode:

	Spl6()  Disable interrupts
	Search read buffer for inode's 
	 packets, unlink them from filled
	 buffer chain
	Unlink inode from net inode chain
	Spl0()  Enable interrupts


Ioctl, FIONREAD
	Spl6()  Disable interrupts
	Search read buffer for first packet for inode
	Record number of bytes in packet
	Spl0()  Enable interrupts
	Report info to user

Read
	Spl6()  Disable interrupts
	Search read buffer for first packet for inode
	Set packet flag N_LOCK
	Spl0()	Enable interrupts
	Check read byte count
	Copy packet to user buffer
	Spl6()	Disable interrupts
	Unlink packet from filled buffer chain
	If read buffer flag N_WANTED is set,
		invoke net read buffer allocate
		and input enable routine
	Spl0()  Enable interrupts
	Report result to user


For Kernel Activity

Read into net buffer 
	Check net status and local net header
	Check and byte swap internet header
	If fragment, look for sibling, 
	 do reassembly bookkeeping, copy 
	 into sibling buffer
	If complete packet, search net inode
	 list for best match
	Update read buffer queue info, link
	 into filled buffer chain
	Signal interrupt enabled process (if one)

	If able to allocate space for next net read,
	 do so, reenable input
	If unable to allocate space for next net
	 read because a needed packet's N_LOCK flag 
	 is set, set packet's N_WANTED flag.

	Note: The code outlined in this section
	will not be interrupted by net read activity 
	because net read is not enabled. 

Dropping packets from the net read buffer 

A packet is dropped from the net read buffer when
	1 - it is found to be bad (e.g. internet
	    header error, lni read error)

	2 - the owner process reads the packet

	3 - the owner process closes the net connection
	    associated with the packet

	4 - no owner process is found for the packet

	5 - more room is needed in the buffer for new,
	    incoming packets


The timeout issue

It may not be necessary to time out packets in
the net read buffer.  For reasons listed above
(particularly 3 and 5), old packets should be
dropped.  I am concerned about the case in 
which a parent with a net connection fds forks a child
and passes a copy of the net fds to the child.  One
of the processes may hang around for a long time
after the other has gone away and may not be the
process which is using the net connection; a
packet for this obsolete connection could be kept 
in the net buffer and could cause confusion.  The 
inode would also be needlessly allocated.  I'd suggest
that we omit packet timeout, for the moment, and I'd 
strongly recommend that net programs which are forked 
close down file descriptors they will not be using.



V.   Connection Definition and Dispatch Rules

   A. TCP Protocol

     1. Definition Rules

	a.  Local socket must be specified.

	b.  Foreign host/socket must both be
	specified or both be NULL.

	c.  Connection must be unique.

     2. Dispatch Rules

	a.  Packet is dispatched to most
	completely defined connection.

   B. User Datagram Protocol

     1. Definition Rules

	a.  If local socket is NULL,
	foreign host/socket must both 
	be NULL.

	b.  If local socket is specified,
	foreign host/socket must both be
	specified or both be NULL.

	c.  Local socket must be unique.

	d.  If foreign host/socket are
	specified, pair must be unique.

     2. Dispatch Rules

	a.  Packet is dispatched via local
	socket, or if no local socket match
	is found, to the UDP connection with
	NULL local socket.

     3. Implications

	a. A potential problem exists with server 
	tftp when duplicate ICP write request packets
	are received (i.e. the foreign host retransmits
	its ICP packet).  When the first ICP packet 
	arrives, the local file is created.  When the
	retransmitted request packet arrives, the server
	tftp will again try to create the local file
	but will find that it already exists and send an 
	error to foreign host/socket from ICP socket
	thus killing off the good transfer.  To
	circumvent this problem, server tftp should
	netopen a completely defined connection (i.e.
	foreign host/socket defined and local socket
	defined) before trying to create the local 
	file.  If the foreign host/socket are the same
	in another connection, netopen will return
	an EACCES error.

   C.  ICMP Protocol (Please note: the following
	definition rules and dispatch rules for
	icmp have not been installed yet.  Icmp
	definition and dispatch are now handled the way
	"other protocols" are handled (see part D.).

     1. Definition Rules

	a.  Foreign host must be NULL.

	b.  "Foreign socket" field may indicate
	the icmp type.

	c.   For icmp type timestamp reply, echo 
	reply and information reply definitions,
	the "local socket" field may indicate the
	icmp identifier. Otherwise, the local
	socket field must be NULL.

	d.  Connection must be unique.

	e.  Please note that icmp type
	echo reply equals 0, which is our
	conventional ignore field when dispatching
	indicator.  So a net connection defined as
	prot2 = icmp protocol and foreign/local
	socket = 0 (NULL), will receive all icmp
	packets which do not match a more refined
	net connection definition.  To receive only
	icmp echo reply packets, the identifier
	field must be nonzero (and must match) in 
	the connection definition and in the incoming 
	packet.

     2. Dispatch Rules

	a.  Packet is dispatched to most completely
	defined connection. 

	b.  An attempt is made to dispatch destination
	unreachable, time exceeded and parameter problem
	icmp packets to the process which sent the original
	packet.  This is done by dispatching the internet
	packet which is inside the icmp packet.

   D.  Other Procotols

     1. Definition Rules

	a.  Foreign host, foreign socket and
	local socket must all be NULL.

	b.  Connection must be unique.

     2. Dispatch Rules

	a.  Packet is dispatched via its internet 
	protocol id.

   Note:  Above rules subject to change.


VI.  Concerns

	Read buffer dynamics may cause confusion
	for application programs.  For instance,
	the program could do an ioctl to find
	out how many bytes are in  the first
	packet for it and later do a read but
	find no data queued for it because its
	packet was dropped from the kernel
	read buffer between the ioctl call and 
	the read call.

	Only one process may be signaled when
	a new packet arrives from the net.

	When a packet in the kernel read buffer
	is read by a user process, the current
	design says the packet will be dropped
	from the kernel buffer.  This would
	cause problems for the case in which
	packets should be dispatched to one
	process for protocol handling and also
	to another monitor process which is
	watching many or all packets coming to 
	the host.

	I'm concerned that too much processing 
	needs to be done when a packet is read in from 
	the net, particularly for an internet fragment,
	before input is reenabled.


VII.  Superficially Resolved Issues

Maximum fragment size between nets and 
subnets -  hardwired into the
kernel.



VIII.  Miscellaneous Insights

It is likely that rudimentary server 
processes, which are waiting for request 
for connection packets for particular 
protocols, may always run.
When the stub process receives a
signal indicating that a packet is
queued for it in the kernel's net read 
buffer, it would fork a child, which
would execl a complete server process.
The execl would pass the net connection
fds as a parameter; the server process
would immediately read the first packet
through this fds and then close the fds.
The server could then open its own net
connection and define a more refined
set of search parameters for its
packets.  The one problem with this
strategy is that the packet intended for
the server process may have been dropped
from the kernel buffer before the server
process gets around to reading it.  But any
process which reads over a net connection
must be prepared to deal with this
"spurious wakeup".