TCP Reassembly Algorithm

			Larry W. Allen

			MIT-LCS-CSC


	This document is a slightly more detailed explanation of the
TCP reassembly algorithm described in the TCP Working Design Document.
The algorithm is given in psuedo-C, using long variable names and
procedure names.

	The important data structures are:
1) The queue of in-sequence received packets, received_data_queue
2) The queue of unacknowledged received packets, received_unacked_queue
3) The received packet presently being processed, received_packet
4) The next expected receive sequence number, receive_sequence_number
A "packet" is contained in a "buffer", which also includes some other
information:
1) The sequence number of the first byte in the packet, packet_sequence_number
2) The length of the data portion of the packet in bytes, packet_length
3) The offset of the first byte of useful data from the start of the
   packet, packet_data_offset

	With this background, the algorithm to sequence TCP segments is
as follows:

procedure tcp_sequence (packet)
{
	if (receive_sequence_number > packet.packet_sequence_number +
				      packet.packet_length) {
		discard_packet (packet)	/* packet is an old duplicate */
		return
	}
	if (packet.packet_sequence_number >= receive_sequence_number