Task stacks are allocated from the process's stack using alloca.  There
is no attempt to recycle stacks on task exit because tasks should rarely
exit and task exits should correlate with process exit.

Tasks only go blocked on "semaphores".  A semaphore is a memory location
containing <number of wakeups on the semaphore> - <number of times task
waiting on the semaphore has been run>.  Only one task may wait on
a given semaphore at one time.  Semaphores may be awakened (by being
incremented) at interrupt (ie. UNIX signal) level.  The process of 
awakening a semaphore must be atomic.  (It looks to me like the semaphore
doesn't need a count, only a flag indicating that a wakeup has occurred.)

Because semaphores are too low-level a mechanism for most purposes,
message queues are provided.  Each message queue is associated with a
semaphore; the process of sending a message causes the associated
semaphore to be awakened.  A "message" consists of five fields:
 	1) link		to the next message in the queue
	2) priority	messages are linked in the queue by priority
 	3) type		messages are typed
 	4) data ptr.	pointer to data being passed in this message
 	5) data len.	length of data being passed in this message

There are two queues of tasks: the runnable queue, and the blocked queue.
Tasks are only moved from the blocked queue to the runnable queue when
the scheduler is run.  The scheduler is only run when a task goes
blocked - there is no preemption.  The scheduler does the following:
	Scan the blocked task list.  For each runnable task, place it
	on the runnable queue in order of priority.  The priority
	that is used is the priority of the first (ie highest priority)
	message on the message queue that the task is waiting for if
	the task is waiting on a message queue.  If the task is waiting
	on just a semaphore, a default priority is used.
	Continue the first task on the runnable task list.
The scheduling MUST be done at the time that a task goes blocked rather
than at the time a wakeup occurs, because the scheduling requires
queue manipulation, and wakeups must be able to occur at interrupt
level.  Since there is no way to defer interrupts in UNIX, only atomic
actions may be performed at interrupt level, and atomic queue manipulations
are not possible on the pdp-11.

The process will only go blocked (outside of I/O operations which always
cause process blocking) inside the scheduler when there are no runnable
tasks.  This will work as follows: a global flag, the "work exists" flag,
is set any time a wakeup occurs.  It is tested by the scheduler using an
atomic test-and-clear operation; if set, the blocked queue and runnable
queue are checked.  If clear the scheduler causes the process to block,
by calling the sysleep () system call.  The length of time to block is
determined in some suitable fashion (possibly from a timeout queue?).

Tasks are probably created by some sort of fork call similar to the
UNIX fork operation. This is because the currently existing coroutine
package uses one.

The structure of a network program will be a main routine which calls
the scheduler initialize routine which in turn calls the "start"
routine as the first task.  The start routine can then fork as needed
to create new tasks.