6. Implementation Details - Send

	Once a connection is open the user program may send and receive
stream data.  This section describes the actions the TCP takes when the
user attempts to send data; the next will describe the actions when he
attempts to receive.

	The first thing any of the user-called TCP routines does on
entry from (and also the last thing before returning to user level) is to
check for the availability of input from the network.  Remember that
the process will be signalled by the kernel network driver when a
packet arrives on one of the process' connections.  The signal-handling
routine simply sets a global flag indicating that network input is
available; this flag is checked when the TCP is entered from user level
and again before returning to user level.

	If the flag show that network input is available, the next
available packet on the TCP connection is read into the next read
buffer on the free read buffer queue.  (In a multiple-connection
version of the TCP, reads would be attempted on each connection).
Normally the free read buffer queue should not be empty; however, it
is possible if the sender is sending less than maximum-size packets.
If there are no free read buffers, the TCP attempts to obtain buffers
from the unacknowedged read queue (that is, the queue of packets which
have been received but not yet acknowledged because they are out-of-
sequence).  Since the unacknowledged read queue is maintained in sequence
number order, the optimization of reusing the last packet on the unack
read queue is performed.  Finally, if no buffers are available on the
unack queue either, the TCP ignores the available packet(s).  The kernel
buffers will eventually be reused (as needed), and the foreign host will
eventually retransmit the dropped packet.

	Assuming that there is a buffer available, the packet is read
in.  Certain validity checks are next performed.  These include:
	1) Checking the TCP checksum
	2) Checking for reset
	3) Process incoming acks:
	   a) If ack is unexpected do a reset.
	   b) Remove send buffers from the send retransmit queue up to the
	      acked sequence number.  If the acked sequence number falls
	      into the middle of a send buffer, slide the data within the
	      send buffer to account for the ack.
	4) Process syn/fin information in the packet.  The details of
	   this are spelled out in the sections on opening and closing
	   the connection.  Note that this actually interacts with the
	   processing of acknowledgments.
	5) Process window information in the incoming packet.  This just
	   involves storing the new window information in the TCB.

	Next the sequence numbers of the incoming data are checked and
the packet is queued on the read data queue (or the receive unacknowledged
queue) as appropriate.  This is discussed in the section on receive
implementation details.

	The processing of received data may indicate that acknowledgment
is necessary.  Acknowledgements are not send at this point; instead they
are held as long as possible.  Acknowledgments will only be sent just before
returning to user level, or upon blocking or sending data.

	Finally, the prolog code checks the timeout queue for timeouts
and processes them.  Each timeout queue entry contains the actual time
the timeout is to go off, the address of a routine to call to process
the timeout, and an argument to pass to that routine.  Timeouts are
defined for several possible events.  First is the retransmission of
packets on the send retransmit queue.  This simply results in the packet
being written out to the net and a new timeout queue entry being made,
up to the maximum number of retransmits.  If the maximum number of
retransmits is exceeded, the connection is aborted and an error returned
to the user.  The second possible timeout event provides for the sending
of delayed acks.  This event is queue when in-sequence data is received,
but the push function is not specified and the receive window which we can
offer is less than half the maximum send window which we posses.
In this case we expect more data to be arriving shortly and thus delay
our acknowledgement until we have something to send or a bigger window
to offer.  If the timeout goes off, the acknowledgement must be sent
immediately to avoid a retransmission by the foreign host.  The third
and final possible timeout is the timeout for the send window opening
up from zero.  If this timeout goes off we have to force a byte of data
into a zero send window, and queue another such timeout.

	This ends the TCP prolog code, which is performed any time the TCP
layer is entered or exited.  Now the send code begins the work of copying
data from the user's buffer into a packet buffer for transmission.  Bytes
are copied from the user's buffer into the current send buffer for the
connection, up to the end of either buffer.  If the end of the user's
buffer is reached, the send call returns with success (after running
the prolog code again to check for packet arrivals and timeouts).