Descriptions of Some of the Algorithms Used in This TCP Implementation

1) Receive window handling - start by advertising max.
 rcv window, as sender uses up window space reduce the
 advertised window until it is 50% of max. advertised window,
 then advertise max rcv window. This strategy avoids silly 
 window syndrome by assuring that the sender occasionally
 really is given a large send window.

	RWINDOW (constant) max. rcv window ever advertised
	rwnd	current advertised rcv window
	rnxt	next expected rcv seqno
	rlast	last expected rcv seqno
	urwnd	useable rcv window

	urwnd = rlast - rnxt;
	if (urwnd < (RWINDOW >> 1)) {
		rwnd = RWINDOW;
		rlast = rnxt + RWINDOW;
		}
	else
		rwnd = urwnd;

2) Send data when available and

 a) when useable send window > 25% advertised window.

 b) or when useable send window < 25% advertised window
  and available data will fit in it.

 c) or every t_retrans number of seconds, when advertised
  send window is 0.

 Strategies a) and b) are also measures to prevent silly window
 syndrome.  Silly window syndrome for the sender occurs when
 t_suna (send unacked seqno) falls way behind t_snxt (send next seqno).

3) Send ACK

 a) when due

 b) or, if have sleep time resolution shorter than current 
 1 second, 
	1) when send data

	2) or when sender's useable window has been reduced to 50%
	of max rcv window; i.e when should update rcv window.

	3) or when rcv PSH bit

	4) or when ACK dally time has expired.

4) Retransmission

Three variables manage retransmission - t_sndtime, t_ntrans,
and t_retrans.  T_sndtime is filled with the current time and
t_ntrans is cleared when t_suna is updated (ch_ack) or when data
is sent starting at t_suna (ch_tcpsnd). Thus this retransmission 
method keeps track
of 1) the time when we transmitted data or 2) the last time
some of our transmitted data was acknowledged. T_retrans is the
number of seconds to wait before retransmitting.  Retransmission
is done when curtime - t_sndtime > t_retrans * (t_ntrans + 1).
When there is no work to be done and t_suna != t_snxt,
sleep time = t_retrans * (t_ntrans + 1) (ch_work).

T_retrans is computed (tt_calc) from a vector of 10 send and
ack times for various seqnos maintained in the t_ttime struct;
from these times round trip delays can be calculated.  If any
round trip time exceeds the current retransmit time (t_retrans),
the retransmit time is increased by 1 second.  In this case we assume
that the retransmit time is shorter than the actual round trip
delay, or the connection is dreadful with lots of lost packets.
If no round trip time exceeds the current retransmit time,
retransmit time = avg. round trip time + 1 second.

If it is necessary to retransmit more than once, time between
retransmissions increases; we use the following algorithm:
	time between retransmits = t_retrans * (t_ntrans + 1)
where t_retrans is no. seconds and t_ntrans is no. times we
have retransmitted. This means that if we allow NTRANS retransmits
of the same data, it takes 
	((NTRANS/2) * (NTRANS * t_retrans)) + ((NTRANS * t_retrans)/2)
seconds to finally timeout.

One big problem with this time management is that our clock
readings truncate to the nearest second so an apparent 1 second
difference in times can, in fact, be anywhere between 16 milliseconds
and 2 seconds less 16 milliseconds.  CSR Unix does have a higher
resolution clock read but it's less convenient to use so, for
now, I'm trying the simpler method.  

Another issue with timing on CSR Unix is that it does not handle
user sleep times of less than 1 second.


5) Special Timeouts

The TCP application may want to ask TCP to close if
it thinks the foreign application has disappeared.

The telnet application, if it has not received any
data from the foreign telnet for a long time, sends
a DO Timestamp option negotiation to the foreign telnet;
if local telnet does not receive a response to this 
option after a specified period of time, it asks
TCP to close the connection because it thinks there is
no application alive at the foreign host.

A second special timeout problem arises when local TCP
has sent a FIN and its FIN has been ACKed (i.e. TCP
is in state FIN_SENT|FIN_ACK) but it has not received
a FIN from the foreign host.  There is a possibility that
the foreign TCP has disappeared and the local TCP should
go away.  We currently let the application level ask TCP
to abort the connection when it finds that 1) it has not
received data in a long time and 2) it is not in data
sending mode.  The application goes out of data sending
mode when it asks TCP to close.


Note:  for more discussion of send and receive window management
and ACK management see D.D. Clark, "Window and Acknowledgement
Strategy in TCP", Internet Protocol Implementation Guide,
Network Information Center, SRI International, Menlo Park, California, 
August 1982.